## Slide 1: Experience with Hypersim on developing Digital Twins of modern power grids
Vinícius Albernaz Lacerda
Lecturer
CITCEA-UPC, Polytechnic University of Catalonia, Barcelona, Spain

## Slide 2: INTRODUCTION
The energy transition is transforming the way we used to control, operate, protect, measure and simulate power systems.
Faster transients occur and reliable measurements/communications are available.
In such a fast-paced context, power grids require a substantial improvement in real-time operation and short-term planning.
Digital Twins can provide fast and accurate predictions on future grid scenarios.

## Slide 3: THE DIGITAL TWIN CONCEPT
A digital twin is a virtual representation of a physical system.
It allows modelling, testing and analysing possible scenarios before applying them in the real world
It can run tools to provide real-time outputs to the physical system based on anticipated behaviour informed by the digital twin.
Source: adapted from https://www.opal-rt.com/digital-twins/
Measurements
Actions
Tool 1
Tool 2
Tool n
Inter-tool communication

## Slide 4: THE HP2C-DT PROJECT - TOOLS
The HP2C-DT project (High-Precision High-Performance Computer-enabled Digital Twins for modern power system applications) aims to investigate the benefits of Digital Twins of power grids.
Large power grids are simulated using High-Performance Computing.
Source: adapted from https://www.opal-rt.com/digital-twins/
Measurements
Actions
Online Stability
Optimal Operation
Adaptive protection
Supercomputer
Real-time equivalents

## Slide 5: THE HP2C-DT PROJECT
Signals exchanged
A2 – Online Interaction
A1 – Online Stability
B1 – Optimal Operation
B2 – Network Equivalents
C – Adaptative Protection
E – Automatic Operation and Control
Real time Power Flow
Actions
Optimal Power Flow
Grid Status
Grid Status
Relays Coordination
Send
Receive
Real Grid
Weather/Forecast
D – Probabilistic Scenario
Restrictions
Real-time data
Short-Circuit Level
Available generation

## Slide 6: COMMUNICATION
Server
Database
Edge Devices
Real-time data
Input actions
Input actions
Real-time data
Visualization
User inputs
Calculations
Results
Data
Ethernet
Quick processing
OPAL-RT/Hypersim
Marenostrum supercomputer
User interface

## Slide 7: SMALL-SIGNAL ANALYSIS TOOL
Examines stability under small disturbances
  Characterize frequency and damping of oscillations
  Identify interactions between network components
Relies on the State-Space model of the grid
  Linearization of EMT differential equations around an operating point
  Modelling time may be unaffordable for large-scale systems
  Automatized modelling and analysis tools are required
State-Space Representation
Pole map
Time-domain linear simulation
Participation factor analysis

## Slide 8: SMALL-SIGNAL ANALYSIS TOOL
The small-signal analysis tool integrated in the DT is based on a modular approach which facilitates the modelling of large-scale power systems.
177 lines
9 transformers
91 loads
28 generator units
etc.
IEEE 118-bus system
Traditional approach
Modular approach
Linearization
State-Space models library
State-Space Model
State-Space Model

## Slide 9: SMALL-SIGNAL ANALYSIS TOOL
The tool is implemented in Python
Libraries: GridCal, Python Control Systems Library
The workflow
Data input
.raw (PSS/E)
Grid topology
Excel
Excel
System data main file
GridCal
Power-flow calculation
Operating
point
State-Space blocks generation
State-Space blocks interconnection
State-Space model
Small-signal analysis
Python Control Systems Library
Small-signal analysis tool
Control parameters
Validation against non-linear EMT simulation
Hypersim

## Slide 10: SMALL-SIGNAL ANALYSIS TOOL
The tool is implemented in Python
Libraries: GridCal, Python Control Systems Library
The workflow
Data input
.raw (PSS/E)
Grid topology
Excel
Excel
System data main file
GridCal
Power flow calculation
Operating
point
State-Space blocks generation
State-Space blocks interconnection
State-Space model
Small-signal analysis
Python Control Systems Library
Small-signal analysis tool
Control parameters
Validation against non-linear EMT simulation
Hypersim

## Slide 11
Constant Input Data
.raw (PSS/E)
Grid topology
Excel
Control parameters
Small-signal analysis
GridCal
Power flow calculation
Sampled Input Data
Operating
point
Control parameters
Equilibrium
point
State-Space blocks generation
State-Space blocks interconnection
State-Space model
Python Control Systems Library
Python DataFrame
Python DataFrame
G(s)
ξ
H2 norm
DC Gains
GridCal
Power flow calculation
Sampled Input Data
Operating
point
Control parameters
State-Space blocks generation
Python DataFrame
Python DataFrame
Python Control
Systems Library

## Slide 12
Space Definition
1° Space Partition
Exploration

## Slide 13
GridCal
Power flow calculation
Sampled Input Data
Operating
point
Control parameters
Python DataFrame
Python DataFrame
P,Q @Load Bus
P,V @Generation Bus
V,θ @Slack Bus
Case Study: 118 Bus System
Define a system set-up
Amount of power installed in each Generation Bus
Peak and minimum total power demand
Loads’ participation factors
System elements:
28 Generation buses
91 Loads buses
172 Lines
9 Transformers
Space Definition

## Slide 14
Sampled Input Data
Operating
point
Control parameters
State-Space blocks generation
Python DataFrame
Python DataFrame
Python Control
Systems Library
P,Q @SG
P,Q @ GFOL
P,Q @ GFOR
Case Study: 118 Bus System
@ GFOL
@ GFOR
System elements:
28 Generation buses
91 Loads buses
172 Lines
9 Transformers
Space Definition

## Slide 15
System elements:
28 Generation buses
91 Loads buses
172 Lines
9 Transformers
Space Definition
Define a system set-up:
Amount of power installed in each Generation Bus
Peak and minimum total power demand
Loads’ participation factors
In each Generation bus, define:
The SG installed power
The CIG installed power
Case Study: 118 Bus System
Dimensions
of the space
Variables for
each dimension

## Slide 16
Space Definition
Total power injected by SGs
Total power injected by CIGs
Total power injected by GFOR-CIGs
Dimensions
of the space
Variables for
each dimension
Power injected by each SG
Power injected by each CIG
Power injected by each GFOR-CIG
Power injected by each GFOL-CIG
-
Variables associated to each non-independent dimension | Not-independent Dimensions |  | Dimensions of the space | Variables associated to each dimension |  | Not-indipendent variables
Power absorbed by each load | Total power demand |  | Total power injected by SGs | Power injected by each SG |  | 
 |  |  | Total power injected by CIGs | Power injected by each CIG |  | Power injected by each GFOL-CIG
 |  |  | Total power injected by GFOR-CIGs | Power injected by each GFOR-CIG |  | 
 |  |  |  | Voltage at each generation bus |  | 
 |  |  |  |  | Power Flow calculation | Reactive Power at each generation bus  proportionally shared among SG, GFOR, GFOL
 |  |  | tau_p of each GFOR-CIG |  |  | 
 |  |  | tau_q of each GFOR-CIG |  |  | 
 |  |  | tau_p of each GFOL-CIG |  |  | 
 |  |  | tau_q of each GFOL-CIG |  |  | 
+
-
+
+

## Slide 17
Space Definition
Total power injected by SGs
Total power injected by CIGs
Total power injected by GFOR-CIGs
Dimensions
of the space
Variables for
each dimension
Power injected by each SG
Power injected by each CIG
Power injected by each GFOR-CIG
Power injected by each GFOL-CIG
-
Variables associated to each non-independent dimension | Not-independent Dimensions |  | Dimensions of the space | Limits | Variables associated to each dimension |  | Not-indipendent variables
Power absorbed by each load | Total power demand |  | Total power injected by SGs |  | Power injected by each SG |  | 
 |  |  | Total power injected by CIGs |  | Power injected by each CIG |  | Power injected by each GFOL-CIG
 |  |  | Total power injected by GFOR-CIGs |  | Power injected by each GFOR-CIG |  | 
 |  |  | Voltage at each generation bus |  |  |  | 
 |  |  |  |  |  | Power Flow calculation | Reactive Power at each generation bus  proportionally shared among SG, GFOR, GFOL
 |  |  | tau_p of each GFOR-CIG |  |  |  | 
 |  |  | tau_q of each GFOR-CIG |  |  |  | 
 |  |  | tau_p of each GFOL-CIG |  |  |  | 
 |  |  | tau_q of each GFOL-CIG |  |  |  | 
Type equation here.

## Slide 18
Space Definition
Total power injected by SGs
Total power injected by CIGs
Total power injected by GFOR-CIGs
Dimensions
of the space
Variables for
each dimension
Power injected by each SG
Power injected by each CIG
Power injected by each GFOR-CIG
Power injected by each GFOL-CIG
-

## Slide 19: SMALL-SIGNAL ANALYSIS TOOL
The application
Power-flow data
State of breakers
Update operating point
Update grid topology
Rebuild State-space model
Perform small-signal analysis
OPAL-RT
¿Stability?
¿Interactions?
Control actions
Small-signal analysis tool
DT

## Slide 20: DT TOOL: Small-signal Stability Constrained Optimal Power Flow
OPF with dynamic constraint, formulated as a data-driven surrogate model of conventional small-signal analysis.
Data-driven surrogate model: regression function fitting the system damping as a function of the quantities describing the operating conditions.
Training data: obtained by computation.

## Slide 21: DT Tool: Small-signal Stability Constrained Optimal Power Flow
OPF with dynamic constraint, formulated as a data-driven surrogate model of conventional small-signal analysis
Data-driven surrogate model: regression function fitting the system damping as a function of the quantities describing the operating conditions
Training data: obtained by computation

## Slide 22: DATA GENERATION
Create a high-information content data set avoiding curse-of-dimensionality:
  Explore the entire operating space of the system (different operating points, different converters’ control modes, etc.)
  Select a limited number of significative samples, by the Latin Hypercube Sampling strategy
  Orient sampling towards the stability margin of the system, by the use of the Entropy function
   Sequential algorithm for efficient data set generation

## Slide 23: DATA GENERATION
* Parallelizable task

## Slide 24: OPTIMAL POWER FLOW
Determine the set of control actions corresponding to the optimal operation point of the power system:
  Information about power flow model and requirements are updated in real-time.
  General formulation to maximize network resilience and performance.
  Parallel computation of future scenarios based on forecast. Several time frameworks can be analyzed.

## Slide 25: ACKNOWLEDGMENT
Questions?
Grant TED2021-130351B-C21 funded by MCIN/AEI/10.13039/501100011033 and, as appropriate, by “ERDF A way of making Europe”, by the “European Union” or by the “European Union NextGenerationEU/PRTR”.
Special thanks to:
UPC group: Eduardo Prieto-Araujo (coordinator), Francesca Rossi, Èlia Mateu, Juan Carlos Olives, Roger Margarit, Soufiane El Yaagoubi,
BSC group: Rosa Badia (coordinator), Francesc Lordan, Eduardo Iraola, Mauro Garcia

## Slide 26: Experience with Hypersim on developing Digital Twins of modern power grids
Vinícius Albernaz Lacerda
Lecturer
CITCEA-UPC, Polytechnic University of Catalonia, Barcelona, Spain